Work, Energy, Power, and Machines	Name _____________________________________________________ Period ___

Work (W = Fd)

1. How much work is done on your car by applying 200 N of force for 12 meters?

2. How much work is done pushing a 500 N object a distance of 10 meters?

3. A box was lifted 8-meters resulting in 129 joules of work, how much does the force was applied (or how much does the box weigh)?

4. A little girl did 125 joules of work when pushing her big brother in his wheelchair with a force of 25- N.  How far did she push him?

5. A 10,000-N cart of a rollercoaster is pushed with 8,000 N of force up a 50-m incline.  How much work was done?

Potential Energy (PE = mgh)

1. An apple has a mass of 0.40 kg and is hanging 3 meters above the ground.  What is its potential energy?

2. A 100 kg object is pulled vertically upward 5.0 m by a rope. Find the work done by the tension force in the rope.

3. How much work is done by a crane lifting a 200.0 kg crate from the ground to a floor 21.0 m above the ground? What is the change in gravitational potential energy of the crate?

4. A 25.6 kg child pulls a 4.81kg toboggan up a hill inclined at 25.7° to the horizontal.  The vertical height of the hill is 27.3 m. Friction is negligible.  Determine the change in potential energy of the toboggan.

5. A 1000-kg cart of a rollercoaster is pushed with up a 50-m incline.  There is a change of 30-m in height. How much potential energy was added to the cart?

Kinetic Energy (KE = ½ mv2)

1. A car with occupants has a mass of 1000-kg.  If it is going 30m/s, what is its kinetic energy?

2. A car with occupants has a mass of 1000-kg.  If it accelerates from 0 to 70 m/s, how much kinetic energy is added?

3. A car with occupants has a mass of 1000-kg.  If it accelerates from 70 to 100 m/s, how much kinetic energy is added to the car?

4. How much kinetic energy must be removed from the 1000-kg car that is going 20 m/s in order to make it stop?  How much for the same car gong 40 m/s or 60 m/s?

5.  A 70-kg man is falling at 70 m/s.  How much kinetic energy is that?

Power (P = W/t = KE/t = PE/t)

1. How much power is done on your car by applying 200 N of force a distance of 12 m in 2 minutes?

2. How much power is used pushing a 500 N object a distance of 10 m in 3 s?

3. A car with occupants has a mass of 1000-kg.  If it accelerates from 0 to 70 m/s in 5.7 s, how much power is used?

4. A car with occupants has a mass of 1000-kg.  If it accelerates from 70 to 100 m/s in 5.7 s, how much power is used?

5. A 15-kg box is carried up a stairs to a floor that is 23-m above the starting location in 43 seconds.  A second person carries an identical box the identical distance in 17 seconds.  How much more powerful is the second person?

Pulley

- Two ropes support the same block (mass of 120-kg).  How much is the tension or force is there in the rope?

- How much force must be exerted to lift the 120-kg block using the pulley system to the right?

- How much force must be exerted to lift the 120-kg block using the pulley system to the right?

- Using the pulley system from #3, you lift a 140-kg sofa 32-meters.  Find the a) Load; b) Load distance;

c) Effort and d) Effort distance?

- Using the pulley system to the right, the load is 480 N and it is lifted 6.0 meters.  What is the a) Load;                                                                 b) Load distance; c) Effort; and d) Effort distance?

- The pulley system with 6 strands probably has a lot of friction and additional mass due to the pulleys.  If you still want to raise the load 5 meters, how much rope do you have to pull?

Ramp

1. A ramp that is 9.2m long takes a force of 180-N to push a cart weighing 250-N up to a platform.  What is the height of the platform?

2. On a ramp 2.5-m long and 0.5-m high, a force of 420-N is being used to push a loaded cart.  How much does the dolly weigh?

Lever

1. A pole is a total of 2-m long and is pivoted 30 cm from a rock that acts as the fulcrum.  If the free end is forced down with a force of 220-N, how much force is exerted on the rock?

2. A jack handle 65-cm long is pivoted at one end and pushed down at the other.  If it exerts a force of 240-N at a point 12-cm from the pivot, find a) the effort force and b) the mechanical advantage.

Efficiency = Work out/Work in

1. To lift a 540-N load a total of 12.0-m, you turn a crank with a force of 110-N pushing it through a distance of 72-m.  What is the efficiency of the machine?

2. Using a machine that is 90% efficient, you have to lift a 1200-N load a total of 3-m.  How much work do you have to do?

3. In a three strand pulley. A 130-kg load is lifted 25-m, using an effort of 540-N.  What is the efficiency of the system?

4. A ramp that is 9.2m long takes a force of 180-N to push a cart weighing 250-N up to a platform that is 4-m above the beginning level.  What is the efficiency of the ramp?