Electricity Review Problems           Name __________________________________________________

| Formulas | P = power (Watts) | V = voltage (Volts) | I = current (Amps) | R = resistance (ohms – Ω) |
| --- | --- | --- | --- | --- |
| Q = charge (Coulomb) | Energy = Work = Pt = (Joules) | V = IR | I = V/R | R = V/I |
| I = Q/t | P = IV | P = I2R | P = V2/R |  |

- What is the power output of a 6-V, 0.5-A bulb?  How many joules of energy are used per second? [3W, 3 J/s]

- Calculate the Power, Current, Voltage and Resistance for each of the following cases.

  - A 60-Ω heater on a 240-V supply

  - A 60-Ω heater with 15-A going through it

  - A 60-Ω heater using 240-W

  - A 12-V car battery delivering 5-A

  - A 5-A current in a 200-W heater coil

  - A 100 W light bulb using 120-V

- Twenty amps pass through a 12-V battery for 3.5-s to start a car.  How much energy is used? [P = 240-W, E = 840-J]

- If the same car from #3 has a mass of 700-kg, how high could this car be lifted (Hint: Potential Energy)? [h = 0.12-m]

- A motor is rated at 250-V, 4-A.  How much energy does it produce in 10 minutes (600-s)? [E = 600,000-J]

- If the motor in #5 loses 30% of the energy as heat, how much heat is produced in that 10 minute period? [Heat = 180,000-J]

- Twelve 20-V bulbs are to be used as decoration.

  - How would you wire them to operate from a 240-V supply – in parallel or in series?

  - If each lamp takes 0.3-A, what is each bulb’s resistance?

- Two lamps are labeled 24-W.  Lamp A is for 12-V and B s for 240-V use.

  - Which has higher resistance?

  - Which has a thicker filament if they are the same length?

- What is the single equivalent resistance for 2766 Ohm, 6656 Ohm, 149 Ohm, and 6388 Ohm connected in series?

- Five 5.90 W Christmas tree lights are connected in series to each other and to an 110V source. What is the resistance of each bulb?

- In the diagram of a series circuit above, suppose R1 and R2 were light bulbs. If the light bulb at R2 burned out, what would happen to the brightness of the light bulb at R1?

- Two resistors, 2.0 ohm and 3.0 ohm, are connected in series with a 12 V battery. Draw the circuit and calculate:

  - the total resistance of the circuit;

  - the current leaving the battery;

  - the current through each resistor;

  - the voltage drop across each resistor.

- In the diagram of a parallel circuit above, suppose R1 and R2 were light bulbs. If the light bulb at R2 burned out, what would happen to the brightness of the light bulb at R1?

- Two resistors, 2.0 ohm and 3.0 ohm, are connected in parallel with a 12 V battery. Calculate:

  - the effective resistance of the circuit

  - the current leaving the battery

  - the current through each resistor

  - the voltage drop across each resistor.

- Three 25 ohms light bulbs and three 100.0 ohms light bulbs are connected in series.

  - What is the total resistance of the circuit?

  - What is their resistance if all six are wired in parallel?